## Slide 1: Organ system modeling
Austin Baird
Department of surgery, division of healthcare simulation sciences
May 9, 2024

## Slide 2
Outline
Model Design of BioGears Engine
Discussion of Sepsis – One Application
System Biology Deep Learning
Notebook Implementation
Brining it Back

## Slide 3
Model and Design
Design a platform for human physiology simulations

## Slide 4: BioGears model overview
Anesthesia Machine:
Ventilator mask or intubation
Equipment leak
Gas sources
Relief valve
Nervous:
Sympathetic/Parasympathetic responses
Pain
Chemo/Baroreceptors
Endocrine:
Hormone regulation models
Epinephrine
Insulin
Glucagon
Want to construct a whole-body model of trauma physiology
Cardiovascular
Blood
Tissue
Extravascular
Respiratory
Renal:
Filtration and urine production
GFR/RBF
Autoregulation
Gastrointestinal:
Nutrient absorption/digestion
Eat meals, drink water
Energy:
Thermal feedback and metabolic demands
Exercise
Environment
Inhaler
Intracellular
Lymph
Drugs:
Administration, kinetics, and dynamics
Opioid
Sedative
Antibiotic
Anesthetic
Hepatic:
Nutrient storage and conversion
Gluconeogensis
Lipogensis

## Slide 5: BioGears Circulation Model
Physics based circulation model: Lumped Parameter (0-D)
Fluid circuit analogue
No spatial element
Properties calculated at each node
  Pressure
  Flow rate
  Volume
Enhancing circuit resolution improves approximation
Lower computational cost than higher fidelity models
Appropriate for global distributions
Decreasing Computational Cost

## Slide 6: BioGears Circuit Model
Cardiovascular Circuit
Renal System
Increased Spatial Resolution of Renal System at a Single Temporal Scale

## Slide 7: BioGears Compartments
Brain
Heart
Arms
Legs
Core
Liver
Gut
Kidneys
Core
Lungs
Vascular Compartments
In total 60 liquid compartments with mapped hierarchy
Tissue Compartments
In total 40 liquid compartments with mapped hierarchy
Pulmonary Compartments
In total 17 gas compartments with mapped hierarchy
Environment Compartments
In total 20 thermal compartments with mapped hierarchy
Miscellaneous Compartments
In total 4 liquid urine compartments, 1 liquid lymph compartment, and 12 gas anesthesia machine and inhaler compartments
Total Compartments
In total 154 total compartments with mapped hierarchy

## Slide 8: Engine Software Architecture

## Slide 9
Sepsis
Using BioGears to construct a whole-body model of sepsis

## Slide 10: Sepsis Overview
  Array of dysregulated physiology in response to infection
    Changes result in sever tissue damage and can be life threatening
  Patient who acquire sepsis in the hospital have a mortality rate of 25% [1]
  Sepsis accounts for 6.2% of the aggregate costs for all hospitalizations [2]
    Around 23.7 billion annually, making it the most expensive condition treated in the hospital [3]
  Detected due to infection analysis and sequential organ failure assessment
    Introduced as part of sepsis-3 definitions [4]
    Still does not fully capture complexity of the syndrome
  Numerous potential mediators, host responses, and organ system interacts affect the evolution of sepsis within an individual patient
    Similarly, there is still no protocol-based resuscitation methods that have shown to improve patient outcomes [5][6][7]
  Want to improve patient outcomes using a mathematical modeling
    Through healthcare simulation
      Training simulations, not computational simulations. May be a manikin, actor, or computer game
    Investigations into possible patient in-silico clinical trials
      Still a very long ways to go

## Slide 11: Motivation: Patient Treatment REFRESH Study
Pink = shared treatment
Grey = control
Red = test
All experimental data taken from [19][20]
Prior to septic shock onset, we administer 500 mL of fluid over an hour
Confirm SBP < 100mmHg
Begin with 4.5 g piperacillin/tazobactam administration intravenously over 30 min
Dose recommended by ICU doctors at UW
Control patient received a second 1000 mL fluid bolus
No norepinephrine administered
Begin maintenance fluids at a rate of 1 mL/kg/h
0.18 ug/kg/min of norepinephrine administered
Maintained at a constant rate
Check SBP, MAP, and urine output each half hour for 6 hours
Introduce additional 500 mL of fluid
UO < 0.625 mL/min
If SBP and MAP exceeded 90mmHg and 65 mmHg we discontinued protocol
Initiated maintenance fluids at 75 mL/hr
We check for UO < 0.625 mL/min,
Supplemental bolus was only 250 mL if UO was not met

## Slide 12: Sepsis Design
(1) The presence of inflammation and tissue damage leads to symptoms of systemic inflammatory response, modeled by general Emax relationships
(2) As damage worsens, the resistances on all vascular-tissue endothelial pathways on the BioGears cardiovascular circuit decrease, leading to hypovolemia and hypoalbumeria and a tendency toward hypotension
(3) Nitric oxide accumulation exerts an additional hypotensive effect
(4) Hypotension induces a response from baroreceptor and glomerular feedback models. Baroreceptor feedback increases systemic vascular resistance (SVR) and heart rate (HR). Glomerular feedback increases fluid retention, causing a drop in urine output (UO) that opposes volume loss
(5) As symptoms of systemic inflammation continue unabated, the ability of baroreceptors to increase SVR becomes inhibited

## Slide 13: Sepsis Design
(1) The presence of inflammation and tissue damage leads to symptoms of systemic inflammatory response, modeled by general Emax relationships
(2) As damage worsens, the resistances on all vascular-tissue endothelial pathways on the, leading to hypovolemia and hypoalbumeria and a tendency toward hypotension
(3) Nitric oxide accumulation exerts an additional hypotensive effect
(4) Hypotension induces a response from baroreceptor and glomerular feedback models. Baroreceptor feedback increases systemic vascular resistance (SVR) and heart rate (HR). Glomerular feedback increases fluid retention, causing a drop in urine output (UO) that opposes volume loss
(5) As symptoms of systemic inflammation continue unabated, the ability of baroreceptors to increase SVR becomes inhibited

## Slide 14: Sepsis Design
(1) The presence of inflammation and tissue damage leads to symptoms of systemic inflammatory response, modeled by general Emax relationships
(2) As damage worsens, the resistances on all vascular-tissue endothelial pathways on the BioGears cardiovascular circuit decrease, leading to hypovolemia and hypoalbumeria and a tendency toward hypotension
(3) Nitric oxide accumulation exerts an additional hypotensive effect
(4) Hypotension induces a response from baroreceptor and glomerular feedback models. Baroreceptor feedback increases systemic vascular resistance (SVR) and heart rate (HR). Glomerular feedback increases fluid retention, causing a drop in urine output (UO) that opposes volume loss
(5) As symptoms of systemic inflammation continue unabated, the ability of baroreceptors to increase SVR becomes inhibited

## Slide 15: Sepsis Design
(1) The presence of inflammation and tissue damage leads to symptoms of systemic inflammatory response, modeled by general Emax relationships
(2) As damage worsens, the resistances on all vascular-tissue endothelial pathways on the BioGears cardiovascular circuit decrease, leading to hypovolemia and hypoalbumeria and a tendency toward hypotension
(3) Nitric oxide accumulation exerts an additional hypotensive effect
(4) Hypotension induces a response from baroreceptor and glomerular feedback models. Baroreceptor feedback increases systemic vascular resistance (SVR) and heart rate (HR). Glomerular feedback increases fluid retention, causing a drop in urine output (UO) that opposes volume loss
(5) As symptoms of systemic inflammation continue unabated, the ability of baroreceptors to increase SVR becomes inhibited

## Slide 16: Sepsis Design
(1) The presence of inflammation and tissue damage leads to symptoms of systemic inflammatory response, modeled by general Emax relationships
(2) As damage worsens, the resistances on all vascular-tissue endothelial pathways on the BioGears cardiovascular circuit decrease, leading to hypovolemia and hypoalbumeria and a tendency toward hypotension
(3) Nitric oxide accumulation exerts an additional hypotensive effect
(4) Hypotension induces a response from baroreceptor and glomerular feedback models. Baroreceptor feedback increases systemic vascular resistance (SVR) and heart rate (HR). Glomerular feedback increases fluid retention, causing a drop in urine output (UO) that opposes volume loss
(5) As symptoms of systemic inflammation continue unabated, the ability of baroreceptors to increase SVR becomes inhibited

## Slide 17
Pathogen invasion and thermal trauma initiate the inflammatory response model
  Infection
    Pathogen originates in tissue where it is combated by local immune mediators
    Inflammation weakens tissue barrier integrity
    Pathogen can enter circulation, leading to systemic inflammatory response (SIRS)
  Burn[2,4]
    Thermal trauma activates systemic inflammatory response
    Inflicts initial hit on global tissue health
Sepsis Design: Inflammation Model

## Slide 18: Sepsis Model: Bacterial Growth and the Immune System
Symbol | Description
Pt | Bacteria at the site of infection, initialized to begin an infection scenario
Mt | Local macrophages at the site of infection
Nt | Local neutrophils at the site of infection
B | The integrity of the local tissue at the site of infection. This barrier must be weakened for neutrophils to migrate to the infection site, facilitates bacteria translocation to the blood
Pb | Bacteria that has diffused to the blood from the infection site
R(t) | State of the toll like receptors, a “switch” that regulates the epithelial barrier integrity of the tissue that the bacteria has infiltrated
NA | Active blood neutrophil population
Extended and adapted model from [10]
  Final term, Pb, is a relationship between the bacterial invasion/growth and the shock model
  How the bacteria in the blood is interacting with circulating blood neutrophils
Hill equations are used to relate the interactions between bacterial and local immune responses
The final equation states that at high bacteria concentrations (above some P+ limit) the switch will be on to allow for neutrophils to the site of the infection
  Low bacterial concentrations the tissue layer blocks the migration of neutrophils

## Slide 19: Sepsis Model: Systemic Inflammatory Response
Symbol | Description
NA/MA | Active blood neutrophil/macrophage population
IL6 | Interleukin-6, later pro-inflammatory mediator which also downregulates TNF
TI | Tissue integrity, ranging from 1 (healthy) to 0 (irreversible damage) Depleted by IL6 and pathogen, moderated by NO
NO | Nitric Oxide, exerts hypotensive activity
TNF | Tumor necrosis factor, early pro-inflammatory mediator, upregulated by MA and NA
Immune response to infection
  We combine work from [11] and [12] and connect the model to our tissue model to induce hypotension, and fluid transport
We include a self-inhibition term to interlukin-6 to guarantee the existence of a stable fixed point
Some equations are omitted for brevity, the complete Acute Inflammatory Model (AIR) can be found in [13]

## Slide 20: Sepsis Model: Microcirculation Model
Inflammatory-mediated tissue damage causes fluid shift and relative hypovolemia
Under normal physiological conditions we can describe this flux to be:
Compute COP using total plasma protein concentration, using the Landid-Pappenhaimer relationship [14]
Use the Patlak equation to determine albumin flux between each vascular-tissue compartment pair [15]
Here sigma is the given tissue reflection coefficient, Pe is the peclet number and we are assuming a constant diffusion capacity (PS) across the entire diffusion distance
We model deterioration of the glycocalyx under severe inflammatory conditions by decreasing the endothelial wall resistance, R1 as a function of TI
  We also decrease the reflection coefficient, sigma

## Slide 21: Results: Model strongly linked to parameterization
Wanted to investigate patient variability to a “moderate” bacterial response
“Susceptible” – Green
  Decrease the rate of phagocytosis by tissue macrophages (kpm parameter)
“Hyperinflammatory” – orange
  Increasing k6m and x66
  Bacteria is eliminated by IL-6 levels remain elevated
“Immunosuppressed” – purple
  Decreasing k6m and x66
  Not a strong inflammatory response but blood bacterial levels remain elevated and tissue integrity continues to deteriorate
From the model:
  k6M (IL-6 recruitment by macrophages)
  x66 (IL-6 self-inhibition)

## Slide 22
System Biology Deep Learning
Ok, we have these large system dynamics described, what do we do with them?

## Slide 23: Motivating Example – Linear Regression
Say we see a strong relationship in the data:
Linear
Logistic
Oscillatory
Ect…
Initial Observations
Define the Model
Proposed Hypothesis:
This looks linear!
Estimate Parameters
Quantify Fit
Test Model
Take your test set and tell me how well you did
Orange for back propagation!

## Slide 24: Motivating Example – Linear Regression
Real example – BMI and Cholesterol we assume to be linear
In fact this was published recently in jama (2023)
  https://www.ncbi.nlm.nih.gov/pmc/articles/PMC10102874/
  “Linear regression was used to study the association between LDL-C and TC level and body mass index standard deviation score (BMI SDS)”
We want a best fit model that minimizes our total error in the model
Note that for this example we don’t know actual function that determines these two things we are hypothesizing there is a linear relationship
Note that our regression model looks quite bad, but if we look at the figure in the JAMA paper is this so different?

## Slide 25: Motivating Example – Polynomial Regression
Here the “true” function is a cosine function
BUT a basis of polynomial functions DOES do a good job over the domain specified
Overfitting is an issue
BUT the coefficients of our fitted polynomial function will mean nothing regarding the true function that describes dynamics
  Only valid within the training domain

## Slide 26: Systems Biology – ODE Model
Now say we don’t have the direct functional relationship,
we have a description of the dynamics evolving over time
  Often informed by some experimental understanding of our system (mechanism)
No closed form solution
Large parameter space
We have a system with parameters p, and observations y which directly measure x and assume some level noise
Question: How is this a potentially problematic formulation?

## Slide 27: Systems Biology – ODE Model
Now say we don’t have the direct functional relationship,
we have a description of the dynamics evolving over time
  Often informed by some experimental understanding of our system (mechanism)
No closed form solution
Large parameter space
We have a system with parameters p, and observations y which directly measure x and assume some level noise
Question: How is this a potentially problematic formulation?
We are assuming the ability to directly measure the system
Test noise might be quantifiable

## Slide 28: Systems Biology – ODE Model Motivation
Why do we want to use NN’s to help our formulation?
Experiments can only measure a subset of our equations
  Glucose concentration
If we only have a subset of dynamics traditional parameter fitting methods may be insufficient
Universal function approximators
  A deep net is one, so why not exploit that?
We have a system with parameters p, and observations y which directly measure x and assume some level noise

## Slide 29: Systems Biology – ODE Model Motivation
What are the cons?
We have a system with parameters p, and observations y which directly measure x and assume some level noise

## Slide 30: Systems Biology – ODE Model
Now we want to use deep learning to either:
Learn the dynamics (or “hidden physics” of the system)
Or learn the parameters
What's special?
Feature layer
  Uses observed basis functions that could potentially describe dynamics
  Scaling of the time domain (normalization)
  Output scaling by the mean
Loss Function
  Three loss function, one that is determined by the ODE
Note: there is no testing for varying feature layer: Is this a problem?

## Slide 31: Systems Biology – ODE Model
Loss Function
  Three loss function, one that is determined by the ODE
The “physics” of the system is embedded in the ode loss function
Still requires integration of the ode
  Using automatic differentiation

## Slide 32: Systems Biology – ODE Model
Now we want to use deep learning to either:
Learn the dynamics (or “hidden physics” of the system)
Or learn the parameters
What's special?
Feature layer
  Uses observed basis functions that could potentially describe dynamics
  Scaling of the time domain (normalization)
  Output scaling by the mean
Note: there is no testing for varying feature layer: Is this a problem?
Why not just include a larger basis? What do we know about this feature layer?

## Slide 33: Systems Biology – ODE Model
To train:
Generate data with our model, adding in some noise (just like we did in our example!)
Only allow for two of the parameters as the training set
Test against noiseless and noisy
Feature layer varies based upon the observed dynamics of the system

## Slide 34: Systems Biology – ODE Model
10% noise added to the sampled space, we see our estimates break down quite a bit
We need to understand how noise impact estimation for these methods
Experimental data is NEVER noiseless
This seems like a red flag….

## Slide 35: Systems Biology – ODE Model
What do the parameters look like on my machine?
There seems to be a reproducibility issue
BUT – just like any nonlinear system, these trained models can approach local min, bifurcations, saddle points, ect…
There are ways to account for this
My learned parameters seem to be at a local minimum

## Slide 36: Systems Biology – Messy Systems, Messy Data
BUT – what data do we have access to?
And what are we modeling?
We want to model the whole-body physiological response to various trauma
AND model treatments during the simulation
This data is messy and almost NEVER measuring the value we want

## Slide 37: Systems Biology – Messy Systems, Messy Data
BUT – what data do we have access to?
And what are we modeling?
We want to model the whole-body physiological response to various trauma
AND model treatments during the simulation
This data is messy and almost NEVER measuring the value we want
How would we use this dataset to learn parameterization of inflammation during trauma?
In theory this is just one observed value of our system (maybe it would work?)
This is the open research question

## Slide 38
Bringing it back
Where are we and where are the gaps?

## Slide 39: Current Work – Opioid Use
Using the data we have –
Whole-body physiology models can be well-validated by existing data
Might not be ready for deep nets…. Yet
Qualitative validation can lead to use cases in simulation and educational training for clinicians

## Slide 40: Current Work – Qualitative Validation for Sim
Clinically-relevant markers for sepsis and septic shock diagnosis according to Sepsis-3[21] definitions*
  Sepsis
    Systolic blood pressure < 100 mmHg
    Respiration rate > 22 (previous slide)
    Renal organ failure assessment score
      UO < 500 mL/day (0.34 mL/min) = 3
      UO < 200 mL/day (0.14 mL/min) = 4
  Septic Shock
    MAP < 65 mmHg
    Serum lactate > 2.0 mmol/L

## Slide 41: Current Work – Curvature as a function of patient state
Can the curvature of patient trajectories inform patient “status”?
For a hemorrhage patient can we triage as a function “turning points”?
Respiration:
Oxygen diffusion
Blood-gas binding
Tissue oxygenation
Tissue:
ATP requirements
Lactate production
Trauma induced inflammation
Circulation:
Pressure and fluid loss
Reperfusion

## Slide 42: Current Work – Patient variability for geriatric anesthesia
Age informs drug clearance, especially acute for older individuals
Anesthesiologist are not well trained on patient response and physiology
Using a whole-body physiology model to construct age-related models

## Slide 43: Computer models for simulation and education
  Get involved!
  https://github.com/DivisionofHealthcareSimulationSciences
  https://github.com/BioGearsEngine/core
  Biogears.dev

## Slide 45: Sepsis Model: Microcirculation Model
Inflammatory-mediated tissue damage causes fluid shift and relative hypovolemia
Under normal physiological conditions we can describe this flux to be:
Compute COP using total plasma protein concentration, using the Landid-Pappenhaimer relationship [14]
Use the Patlak equation to determine albumin flux between each vascular-tissue compartment pair [15]
Here sigma is the given tissue reflection coefficient, Pe is the peclet number and we are assuming a constant diffusion capacity (PS) across the entire diffusion distance
We model deterioration of the glycocalyx under severe inflammatory conditions by decreasing the endothelial wall resistance, R1 as a function of TI
  We also decrease the reflection coefficient, sigma

## Slide 46: BioGears Circuit Model
By considering the fluid-circuit analog, we can use Kirchhoff's laws to solve for the circulation/ventilation using nodal analysis
The current at a given node sums to zero:
Stand up a matrix equation, solve for state of the cardio/pulmonary system